| name | buffer | NaCl concentration | pH |
| --- | --- | --- | --- |
| A5.0n300zd | Sodium acetate | 300 mM | 5.0 |
| Bt6.0n450zd | bis-tris | 450 mM | 6.0 |
| Bt6.5n450zd | bis-tris | 450 mM | 6.5 |
| M6.5n450zd | MOPS | 450 mM | 6.5 |
| P6.5n450zd | Sodium phosphate | 450 mM | 6.5 |
| P7.0n450zd | Sodium phosphate | 450 mM | 7.0 |
| H7.0n450zd | HEPES | 450 mM | 7.0 |
| H7.5n450zd | HEPES | 450 mM | 7.5 |
| T7.7n500zd | tris | 500 mM | 7.7 |

All standard screening buffers contain 10 mM of the buffer, 10 uM ZnSO4, 10 mM DTT, 0.01% NaN3, 1 mM benzamidine, 1x inhibitor cocktail, 5% D2O.